## Slide 2: Discussion Summary
Project Goal: To effectively analyze and simulate street parking around VCU campus.
Similar Studies
Methods
Simulation Creation
Simulation Results Summary
Final Analysis
Conclusion
Questions?

## Slide 3: Similar Studies
Based on 11 Studies
What Parking Analysis Studies attempt to achieve:
  Good size for Parking areas based on constraints
  Proper Street Parking Regulations
  Minimizing Costs of Parking Areas using meters
  Proper Design to reduce traffic flow

## Slide 4: Donald Shoup and No Vacancy
Donald Shoup – Professor in Urban Planning
  Cruising for Parking
  Study explains reasons why parking is important
No Vacancy
  45% of total traffic was cruising for parking in their area
  94% average curb saturation

## Slide 5: Methods
Choosing The Areas
Data Collection Evolution
Calculating Inter-Arrival Rates
Summary Statistics

## Slide 6: Choosing The Areas
Parking Restrictions?
  Meter
  Time Signs
    Hourly
    No Park
  No Restriction
Good visibility
Commuter Student Spots
Decision: 4 Unrestricted, 2 Restricted

## Slide 7: The Areas

## Slide 8: Data Collection
Continuous Stop Watch vs. Non-continuous
Information needed for simulation
  Total number of spots
  Number of spots at time 0
  Times: car arrives, car parks, parked car leaves, car leaves
Data Collection Evolution
  Why it Happened
    Effective recording of the speed of incoming cars.
  Human Ability
    4-6 Entries every 10 seconds

## Slide 9: Data Collection Evolution
Evolution 1
Evolution 2
Evolution 3

## Slide 10: Inter-Arrival Rate Calculation
First and Second Stage Evolution = Simple
Third Stage Evolution = Complex
Simple
  Inter-Arrival = Next Time – Current Time
Complex
  Simple / number of cars = Average inter times
  Current Time + Average Inter times until = Next Time
  VBA Code and Written Notation

## Slide 11: Written Notation

## Slide 12: Inter-Arrival Rate Calc Cont.
The Power of @Risk Software
  Different Distributions
  Rating Criterion
Formatting issues in Excel
  hh:mm:ss not easily recognized
  Change to value than multiply by 60 and 24 to get seconds

## Slide 13: The Power of @Risk
18 Distributions
6 Distribution Tests

## Slide 14: Summary Statistics

## Slide 15: Simulation Creation
Simulation Software based on queueing theory.
  Arena
  Qmms
  MatLab
  VBA
  Siemens PLM Software
  Java
  http://web2.uwindsor.ca/math/hlynka/qsoft.html
    List of 73 different queueing theory software packages

## Slide 16: Simulation Model Logic

## Slide 18: Simulation Results Summary

## Slide 19: Final Analysis

## Slide 20: Number in Queue Comparison

## Slide 21: Regulated Vs. Un-Regulated
4 UNREGULATED AREAS |  |  |  | 
Number of Replications | 50 |  |  | 
replication length | 2909.5 |  | total data collection time: | 
 | Average | Half Width | 11638 seconds | 
Car wishes to park | 9.185 | 0.79 | 3 hours 13 minutes 58 seconds | 
No space available leave | 0.855 | 0.3725 | Average System Time | 
No Park Leave | 175.355 | 2.92 | 48 minutes 29 seconds | 
Parking Area Utilization | 1 | 0 | park prob based on stat sum | 
Time spent in Parking Queue | 1274.465 | 51.065 | 9.66% | 
Average time in system | 220.2538 | 19.845 |  | 
Graph of WIP in queue for park process: | 50 Reps |  |  | 

## Slide 22: Room For Improvements
Park probability maybe larger. During the study illegal and no parking regulated area were accounted for which can skew available spots, and parking probability.
Data Collection:
  Smaller area = more accurate results
  Accounting for a few spots during a time interval
  Account for each spot rather than all of the spots and creating an average for the area.
  Collect during different times of day over several weeks
Simulate based on parking spot rather than parking area

## Slide 23: Conclusive Thoughts
This Project creates a basis for a more in-depth parking study, and describes averages in different areas around VCU.
Cars are parking approx every 4 minutes, and they are arriving approx every 49 seconds.
Street Parking in the selected areas may not be that terrible since parking happens fairly quickly.
An increase in free parking lots will reduce the amount of cruising.

## Slide 24: QUESTIONS